## Slide 1: 3D Point Cloud Visualization

## Slide 2: Tools & libraries for Point Cloud Visualization
1.Open3D: A powerful open-source library for 3D data processing and point cloud visualization.
https://www.open3d.org/
2. MeshLab: An open-source tool for processing and editing 3D triangular meshes and point clouds.
https://www.meshlab.net/
3. Unity 3D: A game development platform that can be used for interactive point cloud visualization.
https://unity.com/
4. PCL (Point Cloud Library): An open-source library for point cloud processing and visualization.
https://pointclouds.org/
5. Matplotlib: A open-source library can be used for basic point cloud visualization.
https://matplotlib.org/

## Slide 3: Tools & libraries for Point Cloud Visualization

## Slide 4: Tools for visualizing pcloud data

## Slide 7
The “mug-only-vertices.ply” file can be download from https://github.com/MatPixel/dataset-for-3d-pointcloud-processing-3d-deep-learning/blob/main/mug-only-vertices.ply

## Slide 8: Visualization using Matplotlib

## Slide 9: Visualization using Open3D

## Slide 11: PCD to Mesh Conversion
WHY?
Surface Reconstruction: Point clouds are collections of discrete points in 3D space, which can be irregularly sampled. Converting them to a mesh creates a continuous surface representation, making it easier to visualize and analyze.
Visualization: Meshes offer smoother and visually appealing representations, ideal for 3D graphics and simulation applications.
Computational Geometry: Meshes simplify geometric algorithms like collision detection and ray tracing, making them more efficient than point clouds.

## Slide 12: PCD to Mesh Conversion
WHY NOT?
Increased Complexity: Meshes have more complex data structures, making some operations more challenging.
Mesh Artifacts: Meshes can have artifacts like gaps or non-manifold geometry, depending on the reconstruction method.
Information Loss: Converting to meshes can lose fine-grained details from the original point cloud.

## Slide 13: PCD to Mesh Conversion: CODE
# Import libraries import numpy as np import open3d as o3d # Load a point cloud ply_file_path_read = "bunny-pcd.ply" point_cloud = o3d.io.read_point_cloud(ply_file_path_read) # Compute normals if PCD does not have if point_cloud.has_normals() == False: print("Estimating normals...") point_cloud.estimate_normals() else: print("PCD already has normals. So, skip estimating normals") # Orient the computed normals w.r.t to the tangent plane. # This step will solve the normal direction issue. If this step is skipped, there might be holes in the mesh surfaces. o3d.geometry.PointCloud.orient_normals_consistent_tangent_plane(point_cloud, 10) # Estimate radius for rolling ball distances = point_cloud.compute_nearest_neighbor_distance() avg_dist = np.mean(distances) radius = 1.5 * avg_dist print("Minimum neighbour distance = {:.6f}".format(np.min(distances))) print("Maximum neighbour distance = {:.6f}".format(np.max(distances))) print("Average neighbour distance = {:.6f}".format(np.mean(distances))) mesh = o3d.geometry.TriangleMesh.create_from_point_cloud_ball_pivoting( point_cloud, o3d.utility.DoubleVector([radius, radius * 2])) print("PCD Detail: {}".format(point_cloud)) print("Mesh Details: {}".format(mesh)) # Visualize and save the mesh generated from point cloud #mesh.paint_uniform_color(np.array([0.5, 1.0, 0.5])) # to uniformly color the surface o3d.visualization.draw_geometries([mesh], window_name='mesh with estimated normals', width=1200, height=800) o3d.io.write_triangle_mesh("bunny-pcd-to-mesh.ply", mesh, write_ascii=True)

## Slide 14: The output

## Slide 15: PCD to Voxel Grid Conversion
WHY?
Regularization: Point clouds are often irregularly sampled. Converting them to a voxel grid imposes a regular structure, providing a more organized and standardized representation of the 3D space.
Quantization: Voxel grids quantize the 3D space into small cubes (voxels). This simplifies spatial indexing, allowing for efficient and uniform data processing.
Resampling: Voxel grids enable uniform resampling of the 3D space, allowing you to change the voxel size to control data resolution.
Medical Imaging: Voxel grids are used in medical imaging for representing volumetric data, such as CT scans and MRI images.

## Slide 17: PCD to Voxel Grid Conversion
WHY NOT?
Complexity: Voxel grids introduce additional data structures and indexing mechanisms, increasing computational complexity for certain operations.
Information Loss: Fine-grained details present in the original point cloud can be lost depending on the voxel size.

## Slide 18: PCD to Voxel Grid Conversion
# Import libraries import numpy as np import open3d as o3d # Load a point cloud ply_file_path_read = "bunny-pcd.ply" point_cloud = o3d.io.read_point_cloud(ply_file_path_read) #point_cloud = point_cloud.uniform_down_sample(every_k_points=10) # if there are huge points point_cloud.scale(1 / np.max(point_cloud.get_max_bound() - point_cloud.get_min_bound()),center=point_cloud.get_center()) # Fit to unit cube o3d.io.write_point_cloud("bunny-pcd-unitcube.ply", point_cloud, write_ascii=True) # Estimate radius for rolling ball distances = point_cloud.compute_nearest_neighbor_distance() avg_dist = np.mean(distances) print(f"Average neighbour distance = {np.mean(distances):.6}") # Guess different voxel sizes based on points' distances voxelsize = np.round(avg_dist, 5) voxelsize_half = voxelsize/2 voxelsize_double = voxelsize*2 print(f"Different voxel size considered based on points' distances: {voxelsize}, {voxelsize_double}, {voxelsize_half}") voxel_grid = o3d.geometry.VoxelGrid.create_from_point_cloud(point_cloud, voxel_size=voxelsize) print(f"Voxel center in X,Y,Z = {voxel_grid.get_center()}") print(f"Sample Voxels: \n {voxel_grid.get_voxels()[:3]}") o3d.visualization.draw_geometries([voxel_grid], width=1200, height=800) o3d.io.write_voxel_grid("bunny-pcd-to-voxel-001-unitcube.ply", voxel_grid, write_ascii=True) voxel_grid = o3d.geometry.VoxelGrid.create_from_point_cloud(point_cloud, voxel_size=voxelsize_half) o3d.visualization.draw_geometries([voxel_grid], width=1200, height=800) o3d.io.write_voxel_grid("bunny-pcd-to-voxel-002-unitcube.ply", voxel_grid, write_ascii=True) print(f"Voxel center in X,Y,Z = {voxel_grid.get_center()}") print(f"Sample Voxels: \n {voxel_grid.get_voxels()[:3]}") voxel_grid = o3d.geometry.VoxelGrid.create_from_point_cloud(point_cloud, voxel_size=voxelsize_double) o3d.visualization.draw_geometries([voxel_grid], width=1200, height=800) o3d.io.write_voxel_grid("bunny-pcd-to-voxel-003-unitcube.ply", voxel_grid, write_ascii=True) print(f"Voxel center in X,Y,Z = {voxel_grid.get_center()}") print(f"Sample Voxels: \n {voxel_grid.get_voxels()[:3]}")

## Slide 19: PCD to Voxel Grid Conversion
Plots from left to right and top to bottom: voxel grid with voxel size = 0.00644, 0.01288, 0.00322 and the combined one respectively.

## Slide 20: Visualizing 3D meshes
# Import libraries import numpy as np import open3d as o3d # Load a mesh ply_file_path_read = "bunny-mesh.ply" mesh = o3d.io.read_triangle_mesh(ply_file_path_read) mesh.compute_vertex_normals() #mesh.scale(1 / np.max(mesh.get_max_bound() - mesh.get_min_bound()),center=mesh.get_center()) # Fit to unit cube print(f"Number of Vertices = {len(np.asarray(mesh.vertices))}") print(f"Number of Triangales(faces) = {len(np.asarray(mesh.triangles))}") # Convert mesh to pcd points = mesh.vertices point_cloud = o3d.geometry.PointCloud(points) # Visualize and save the point cloud o3d.visualization.draw_geometries([point_cloud], width=1200, height=800) o3d.io.write_point_cloud("bunny-mesh-to-pcd.ply", point_cloud, write_ascii=True)
From the above code, the commented line is meant to make the mesh fit into a unit cube by scaling around the center. This step is often used in real-time projects where multiple meshes are involved for processing.
#mesh.scale(1 / np.max(mesh.get_max_bound() - mesh.get_min_bound()),center=mesh.get_center()) # Fit to unit cube

## Slide 21: Meshes to PCD Conversion

## Slide 22: Meshes to Voxel Grid
# Import libraries import numpy as np import open3d as o3d # Load a mesh ply_file_path_read = "bunny-mesh.ply" mesh = o3d.io.read_triangle_mesh(ply_file_path_read) mesh.compute_vertex_normals() mesh.scale(1 / np.max(mesh.get_max_bound() - mesh.get_min_bound()),center=mesh.get_center()) # Fit to unit cube print(f"Number of Vertices in the mesh = {len(np.asarray(mesh.vertices))}") print(f"Number of Triangles(faces) in the mesh = {len(np.asarray(mesh.triangles))}") o3d.io.write_triangle_mesh("bunny-mesh-unitcube.ply", mesh, write_ascii=True) # Compute points distances pcd = o3d.geometry.PointCloud() pcd.points = o3d.utility.Vector3dVector(mesh.vertices) distances = pcd.compute_nearest_neighbor_distance() avg_dist = np.mean(distances) print(f"Average neighbour distance = {np.mean(distances):.6}") # Guess different voxel sizes based on points' distances (KDTree approach also can be used) voxelsize = np.round(avg_dist, 5) voxelsize_half = voxelsize/2 voxelsize_double = voxelsize*2 print(f"Different voxel size considered based on points' distances: {voxelsize}, {voxelsize_double}, {voxelsize_half}") # Convert mesh to pcd voxel_grid = o3d.geometry.VoxelGrid.create_from_triangle_mesh(mesh, voxel_size=voxelsize) print(f"Voxel center in X,Y,Z = {voxel_grid.get_center()}") print(f"Number of voxels = {len(np.asarray(voxel_grid.get_voxels()))}") print(f"Sample Voxels: \n {voxel_grid.get_voxels()[:3]}") o3d.visualization.draw_geometries([voxel_grid], width=1200, height=800) o3d.io.write_voxel_grid("bunny-mesh-to-voxel-001-unitcube.ply", voxel_grid, write_ascii=True) voxel_grid = o3d.geometry.VoxelGrid.create_from_triangle_mesh(mesh, voxel_size=voxelsize_half) print(f"Voxel center in X,Y,Z = {voxel_grid.get_center()}") print(f"Number of voxels = {len(np.asarray(voxel_grid.get_voxels()))}") print(f"Sample Voxels: \n {voxel_grid.get_voxels()[:3]}") o3d.visualization.draw_geometries([voxel_grid], width=1200, height=800) o3d.io.write_voxel_grid("bunny-mesh-to-voxel-002-unitcube.ply", voxel_grid, write_ascii=True) voxel_grid = o3d.geometry.VoxelGrid.create_from_triangle_mesh(mesh, voxel_size=voxelsize_double) print(f"Voxel center in X,Y,Z = {voxel_grid.get_center()}") print(f"Number of voxels = {len(np.asarray(voxel_grid.get_voxels()))}") print(f"Sample Voxels: \n {voxel_grid.get_voxels()[:3]}") o3d.visualization.draw_geometries([voxel_grid], width=1200, height=800) o3d.io.write_voxel_grid("bunny-mesh-to-voxel-003-unitcube.ply", voxel_grid, write_ascii=True)